SCIENCE AND ENGINEERING RESEARCH COUNCIL

 RUTHERFORD APPLETON LABORATORY
 INFORMATICS DIVISION

 OS 4000 USER NOTE 105

 ____________________________________________
 Kermit-40 for GEC OS4000(RAL),   Version 3.5
                                                                 issued by
                                                                 M J Loach

                                                                March 1986
 _________________________________________________________________________



                                 ABSTRACT


         Kermit is an error protected, asynchronous file transfer protocol
 designed by Columbia University, USA, intended  to  work  over  RS232/V24
 interfaces.  It  is  widely  used  as a 'standard' means of file transfer
 between micro-computers and other  micro-computers  or  larger  machines.
 Any two  machines which have Kermit implemented on them can transfer text
 files, (and sometimes also binary files) provided the necessary  hardware
 inter-connection is  provided.   Kermit-40  is the implementation for GEC
 4000 series computers running under RAL OS4000, and  provides  the  means
 whereby Kermit  on  micro  (or  larger)  computers  can transfer text and
 binary files with OS4000 machines.




















 Kermit distribution policy requires that permission hereby be granted  to
 any individual  or  institution  to  copy  or  use  this document and the
 programs described in it, except for explicitly commercial purposes.









                             _________________
                             Table of Contents



 1   Preface.............................................................1
   1.1   Revisions for Version 3.2.......................................1
   1.2   Revisions for Version 2.1.......................................2

 2   Introduction........................................................4

 3   Running Kermit-40...................................................7

 4   The command list....................................................7

 5   The commands, in detail.............................................9
   5.1   To send a file, or files, to micro-kermit.......................9
   5.2   To receive files from micro-kermit.............................10
   5.3   To reset default parameters....................................10
       5.3.1   DEBUG (off/on)...........................................12
       5.3.2   EOL n....................................................12
       5.3.3   STX n....................................................13
       5.3.4   PAD n....................................................13
       5.3.5   CHAR n...................................................13
       5.3.6   SEND n...................................................13
       5.3.7   RETRYS n.................................................13
       5.3.8   TIME n...................................................13
       5.3.9   TIMEOUT n................................................14
       5.3.10   QUOTE n.................................................14
       5.3.11   8BIT n..................................................14
       5.3.12   BINARY (off/on).........................................14
       5.3.13   REPEAT..................................................14
       5.3.14   NORMAL (on/off).........................................15
   5.4   To display the settings of SET parameters......................15
   5.5   To switch Kermit-40 into remote Server mode....................16
   5.6   To obtain on-line help on the Kermit-40 commands...............17
   5.7   To exit from Kermit-40.........................................17

 6   Examples of using Kermit-40........................................18
   6.1   Example- Kermit-40/IBM PC (Telios).............................18
   6.2   Example- Kermit-40/IBM PC (Kermit-MS)..........................20
   6.3   Example- Kermit-40/ VAX/VMS (Kermit-32)........................23

 7   What to do when things go wrong....................................25
   7.1   Failure to be able to Connect to host..........................25
   7.2   Failure of the transfer of the file(s).........................25

 8   Appendix A.........................................................26











                           Kermit-40 Users Guide


     _______
 1   Preface                                                               |
                                                                           |
       _________________________
 1.1   Revisions for Version 3.2                                           |
                                                                           |
     This version of Kermit-40 provides the following:                     |
                                                                           |
                                                                           |
     Main features:                                                        |
                                                                           |
 *   Inclusion of Server mode.                                             |
                                                                           |
 *   Repeat count prefixing available.                                     |
                                                                           |
 *   Receive command can be specified with a filename.                     |
                                                                           |
 *   A file of initialising commands can be read at the start of a  Kermit |
     run, as provided for in some Kermits as a 'TAKE' file.                |
                                                                           |
 *   Packets of upto 94 characters can now be sent, and upto 80 characters |
     can be received.                                                      |
                                                                           |
                                                                           |
     Bugs fixed:                                                           |
                                                                           |
 *   Overprints were still output to &KERMLOG, this has been fixed.        |
                                                                           |
 *   Error messages from the Send command were incorrect.                  |
                                                                           |
 *   I/O buffers have been enlarged, to prevent  overwriting  problems  in |
     &KERMLOG.                                                             |
                                                                           |
 *   Eight bit quoting is now handled whenever agreed, irrespective of the |
     SET BINARY option.                                                    |
                                                                           |
 *   The code has been altered so that the standard GEC version  will  now |
     compile.                                                              |
                                                                           |
 *   Prefix encoding and decoding is now done on file header packets.      |
                                                                           |
 *   A check has been included to prevent text file records received  from |
     exceeding 235 characters.                                             |
                                                                           |
                                                                           |
     General improvements:                                                 |
                                                                           |
 *   The Data Management error code after a DMCONNECT is  now  written  to |
     &KERMLOG.                                                             |
                                                                           |
 *   Conversion of file names to 'normal form' can now be switched off.    |
                                                                           |
 *   Output from the SHOW command displays off/on instead of 0/1.          |
                                                                           |
 *   In Receive, the message 'oldname receiving  as  newname'  appears  in |
     &KERMLOG.                                                             |


 March 1986                                                      Page    1
                           Kermit-40 Users Guide


                                                                           |
                                                                           |
       _________________________
 1.2   Revisions for Version 2.1

     This release of Kermit-40 is a more complete version  of  the  Kermit
 protocol.  There  are  two  added  main  features,  eight bit quoting for
 binary file  transfer,  and  the  ability  to  timeout  failed   protocol
 exchanges.  A  number  of  bug  fixes  and  other  improvements  are also
 incorporated.


     Main features:

 *   Binary file transfer included, with an eight bit quoting ability.

 *   10 second timeout added, with SET timeout facility included.


     Bugs fixed:

 *   Message output when number of  packet  retries  exceeds  the  maximum
     allowed.

 *   Help can be abreviated to 'h' instead of 'he'.

 *   Parameters can be abbreviated sensibly.

 *   Overprint control records no longer appear in the logfile.

 *   A command field consisting of only spaces is now treated  as  a  null
     command instead of causing Exit.

 *   ASCII character Delete is now transferred correctly.

 *   If a transfer was aborted by the micro-kermit, and a  subsequent  one
     started, Kermit-40 could crash.  This should be fixed.


     General improvements:

 *   Parameter MAXTRY is renamed to RETRYS.

 *   Parameters IMAGE and REMOTE are redundant  and  therefore  have  been
     removed.

 *   Parameter DEBUG now prints hex values in 8 digits instead of 6.

 *   Parameter SEND should  be  specified  in  seconds  instead  of  milli
     seconds.

 *   Checks are made for correct filetype on opening files, (types LST and
     LSB ).

 *   Checks are made for legal timeout periods,  both  for  those  entered


 Page    2                                                      March 1986
                           Kermit-40 Users Guide


     with SET and the one received in the initialisation exchange.

 *   The logfile is now called &KERMLOG instead of  USER.KERMLOG,  and  is
     not deleted by Kermit-40.

 *   All error packets have 'Kermit-40' prefix, and will be written to the
     logfile.


 ____________________
 Binary file transfer


     OS4000 files with an attribute of type LSB have a concept of variable
 length records.  Records are normally of a length determined by the  size
 of data  block  written  by  each Babbage write statement in a particular
 program.  Most other operating systems treat a binary image as  a  stream
 of bytes  with  no  record  terminators,  hence  Kermit cannot be used to
 transfer binary files while retaining this record information.

     Whilst transfer of binary  image  streams  from  other  computers  to
 OS4000 and  back again will involve the use of records in the GEC file, a
 correct binary image without records will be  returned  to  the  computer
 receiving the files back again.  However, if an LSB file originating from
 OS4000 is  sent away to another machine with Kermit, and then returned to
 a GEC machine, the record structure will not be preserved in the original
 fashion.  Thus such a file will no longer be useable in the orginal sense
 under OS4000.

     Since the binary transfer facility is expected to  be  used  for  the
 movement of binary images between machines other than GECs, where the GEC
 machine is  purely  acting  as  carrier,  this  is  not expected to be of
 concern.  It seems very unlikely that anyone would want to use  Kermit-40
 for the  transfer of OS4000 image files, but if they did then it would be
 possible to use COPY with OPT BTOT to create a text listing of the  file,
 which could  then  be transferred to another machine via Kermit, and then
 rebuilt in the same way using OPT TTOB.




















 March 1986                                                      Page    3
                           Kermit-40 Users Guide


     ____________
 2   Introduction

     Kermit-40 is the RAL GEC implementation of the Kermit  file  transfer
 protocol   as  devised  by  Columbia  University  Centre  for   Computing
 Activities, USA.  It is written to run  under  OS4000(RAL  modified)  and
 enables transfers  between  a GEC machine and any asynchronously attached
 micro, also running Kermit.  To transfer files, a version of Kermit  must
 be present  on  both machines involved.  There is a version available for
 most current computer systems, many of which can be obtained all together
 on magnetic tape from Columbia University.  However,  some  sites  in  UK
 maintain a  current  on-line  version  of the tape, often including other
 extra versions which are too new to be included on the Columbia tape.  It
 is useful to look at the filestore of one of these  sites,  and  possibly
 even to  register  on  their electronic mailing list, particularly if you
 are going to use Kermit a lot.  The exchange  of  experience,  ideas  and
 talk of new versions is worth following.

     The protocol is based on the use of packets, which are chunks of data
 with leading and trailing information added indicating the type of packet
 and helping with error protection.  Packets are often about the length of
 one line on a display terminal, and they can be accepted or  rejected  by
 the receiving  Kermit.   There  are  different  types of packets, not all
 contain file data, some are for acknowledgment/rejection  purposes  only,
 others may  contain  initialisation  parameters  or error messages.  Data
 packets contain sequential fragments of the file, often  of  about  70-80
 characters in  length,  with  some protocol information appended 'around'
 them.  There is a checksum character, which is calculated from the  whole
 of the  data  in  one packet, and appended to the end of that packet.  If
 errors occur in transmission, then the checksums will  be  different  and
 the packet would be rejected for re-sending.

     By means of this protected packet system, errors can rarely occur  in
 files.  However  users  should  be aware that there are ways it can fail,
 even though the file may appear to transfer correctly.  This  can  happen
 as the  result of multiple separate errors occuring which are opposite in
 effect in the same packet, which then preserve the correct value  of  the
 checksum.

     All Kermit packets are made up from printable characters only.  There
 are no control characters used by the protocol, except for the  beginning
 of packet  marker  and  the  end-of-line  (end-of-packet)  character,  by
 default ASCII 1 and  13  respectively.   Kermit  transforms  any  control
 characters which  appear in data, into printable representations, using a
 technique called control-quoting.  When data is to  be  transferred  with
 eight bit  values  then  'eighth  bit quoting' will also be used.  Repeat |
 count prefixing is available in order to  provide  data  compression  and |
 therefore greater efficiency over communication lines.                    |

     Kermit-40 can operate as a remote Server, and once in this mode,  the |
 user is  able  to send and receive files at will by issuing commands only |
 from the local Kermit, without having to 'Connect'  back  to  the  remote |
 Kermit.                                                                   |




 Page    4                                                      March 1986
                           Kermit-40 Users Guide


 ____________
 Reading note

     In any documentation on the use of Kermit, it  is  convenient  to  be
 able to  refer  separately  to  the two Kermits which are to talk to each
 other.  Therefore, from here onwards,  the  Kermit  running  on  the  GEC
 machine will  be  referred  to  as Kermit-40, and that on your micro/mini
 will be referred to as micro-kermit.

     In addition, this guide particularly refers to the version of  Kermit
 known as  Kermit-40,  written for use on the GEC MUMs in SERC, and should
 be regarded as  supplementary  to  the  fuller  versions  of  the  Kermit
 documentation as  distributed  by  Columbia University.  They provide two
 documents, the protocol manual, and the user manual, in addition to other
 supplementary documents.  Recent versions are available on line, and full
 details of how to read them can be obtained from ICF User  Support.   All |
 queries relating to Kermit-40 specifically should be addressed to         |
                                                                           |
 Martin J Loach                                                            |
                                                                           |
 Mail addresses NSIN12 @ UK.AC.RL.GB or via SUPPORT @ UK.AC.RL.GB,         |
                                                                           |
 or at                                                                     |
                                                                           |
 ICF User Support,                                                         |
 Rutherford Appleton Laboratory,                                           |
 Chilton,                                                                  |
 Didcot,                                                                   |
 Oxon,                                                                     |
 OX11 0QX.                                                                 |
                                                                           |
 Telephone Abingdon (0235) 446252.                                         |

 ______________________________
 Kermit-40 implementation notes

     Version 3.2  of  Kermit-40  is  not  a  full  implementation  of  any
 particular version  of the Kermit protocol, but has been based on Version
 2 and the structure of the prototype program followed that of the UNIX  C
 listing.  It embraces most of the essential parts needed to transfer text
 and binary files successfully with other Kermits of any generation, since
 Kermits should always be upward-compatible.

     There are a number of restrictions which the user familiar with other
 Kermits should be aware of.  Kermit-40 works in  REMOTE  mode  only,  and
 therefore has  no  CONNECT command.  No Image mode is possible due to the |
 restrictions of the RAL OS4000 communications format using  even  parity. |
 However 8-bit quoting is available for binary transfers.  There is no '?' |
 help facility,  although  a  limited  'HELP' command is available.  Error |
 checks are done with single character  checksumming,  no  other  type  is |
 supported.                                                                |







 March 1986                                                      Page    5
                           Kermit-40 Users Guide


 Kermit-40 Capabilities at a glance:                                       |
                                                                           |
 Local operation:                   No                                     |
 Remote operation:                  Yes                                    |
 Transfers text files:              Yes                                    |
 Transfers binary files:            Yes                                    |
 Wildcard send:                     No                                     |
 ^X/^Y interruption:                No                                     |
 Filename collision avoidance:      No                                     |
 Can time out:                      Yes                                    |
 8th-bit prefixing:                 Yes                                    |
 Repeat count prefixing:            Yes                                    |
 Alternate block checks:            No                                     |
 Terminal emulation:                No                                     |
 Communication settings:            No                                     |
 Transmit BREAK:                    No                                     |
 IBM mainframe communication:       No                                     |
 Transaction logging:               Yes                                    |
 Session logging:                   No                                     |
 Raw transmit:                      No                                     |
 Act as server:                     Yes                                    |
 Talk to server:                    No                                     |
 Advanced server functions:         No                                     |
 Advanced commands for servers:     No                                     |
 Local file management:             No                                     |
 Handle file attributes:            No                                     |
 Command/init files:                Yes                                    |
 Command macros:                    No                                     |




























 Page    6                                                      March 1986
                           Kermit-40 Users Guide


     _________________
 3   Running Kermit-40

     Normally micro-kermit will be invoked on the local machine, using the
 procedures given  in  the  documentation  for  that  version.   Once  the
 hardware connection has been established to the remote GEC computer, then
 the CONNECT  command  will be used on the micro-kermit, enabling login to
 the GEC in the usual manner, the micro emulating a terminal.

     Once logged in Kermit-40 is started on the GEC machine by the command
 RARESYS.KERMIT .  The proforma is:

                RARESYS.KERMIT IN   = stream 1 (*) -                       |
                               OUT  = stream 2 (*/NEW)                     |
                               WITH = stream 5 (SINK)                      |
                                                                           |
 Arguments:                                                                |
                                                                           |
 IN   The input stream for commands and reception from  the  micro-Kermit. |
                                                                           |
 OUT  The output stream used for messages  and  for  transmission  to  the |
      micro-kermit.                                                        |
                                                                           |
 WITH The input stream used for initialisation purposes, which may contain |
      Kermit commands, and is read when Kermit-40 first starts up.         |
                                                                           |
 Other streams:                                                            |
                                                                           |
 3    The input stream  used  for  reading  OS4000  files  being  sent  to |
      micro-kermit.                                                        |
                                                                           |
 4    The output stream used for writing files received by Kermit-40.      |
                                                                           |
 6    The output stream used for writing &KERMLOG, the log file.           |


 The prompt will appear thus:

 KERMIT-40>

     ________________
 4   The command list

     A number of commands are available  to  set  up,  and  initiate  file
 transfers.

     ____
     SEND

     Initiate the sending of a file(s) from the GEC to micro-kermit

     _______
     RECEIVE

     Initiate the reception of a file(s) to be sent from micro-kermit.





 March 1986                                                      Page    7
                           Kermit-40 Users Guide



     ___
     SET

     Alter various  default  parameters which MAY need to be set according
     to the micro and communications hardware etc in use.

     ____
     SHOW (also STATUS)

     Display the current values of all parameters.

     ______
     SERVER                                                                |
                                                                           |
     Switch Kermit-40 into Server mode, further commands  are  taken  from |
     the micro-kermit.                                                     |

     ____
     HELP

     Obtain help  by  listing  the  commands  available  and/or  by giving
     further information on a particular command.

     ____
     EXIT (also QUIT/END/BYE)

     End the Kermit program.


     All commands can  be  safely  abbreviated  to  the  least  number  of
 characters required to make the command unique.  However, abbreviating to
 less will  not  produce  an  error  message,  the  command chosen will be
 according to the priority given above.  Case has no significance, and any
 parameters are separated by one or more spaces.  There may appear  to  be
 some similarity  to  CAMTEC  PAD  commands,  but  any such duplication is
 purely coincidental.
























 Page    8                                                      March 1986
                           Kermit-40 Users Guide



     _______________________
 5   The commands, in detail

           __________________________________________
     5.1   To send a file, or files, to micro-kermit.

     SEND command

     Format:

         SEND[ filename][ filename filename...]

     where 'filename' is a valid OS4000 filename (default %C),

     For example:

         send .klog me.mjl.text

     will send  the  two  files,  .klog  in  the  current  directory,  and
     .mjl.text in the top directory.

         Each file will be sent separately, but automatically.  Unless Set |
     Normal Off has been specified, Kermit-40 will form a simple  filename |
     from each  file identifier, which will be sent to micro-kermit at the
     start of each file transfer, and used by micro-kermit  as  the  local
     filename to  be  created.   The full OS4000 identifier is stripped of
     all leading directory structures  including  the  leading  full-stop.
     Thus, for  example,  NSIN99.MACRO.TEST will become TEST, which is the
     simplest form  of  file  name  which  should  be  useable   by   most
     micro-kermits.

         There will be, by default, a 15 second  delay  before  the  first
     packet is  sent,  during  which period the user should escape back to
     micro-kermit (ie  escape  from  CONNECT  mode  on  the  micro-kermit,
     generally something  like  control-]  C  ), and switch that Kermit to
     RECEIVE.  The transfer should then take place, and on completion, the
     user should  return  the  micro-kermit  to  CONNECT  mode,  whereupon
     further commands  can be given to the outstanding KERMIT-40 prompt on
     the GEC machine.

         It is possible  that  if  the  user  is  too  slow  returning  to
     micro-kermit at  the  start  of  sending  then  the first packet from
     Kermit-40 could be missed.  If this happens, then the transfer should
     eventually proceed normally after micro-kermit or Kermit-40 has timed
     out and sent some NAK (negative-acknowledgment) packets.  Be patient,
     don't give up 'till Kermit does, as indicated on  your  screen  by  a
     message something  like,  'Too  many  retries'.  If the transfer does
     really fail, then use CONNECT to return to Kermit-40, which may still
     be in SEND mode.  If so, indicated by the failure of  the  prompt  to
     appear when  pressing  <RETURN>, then control Z <RETURN> should allow
     Kermit-40 to be aborted, which must then be restarted before  further
     attempts can be made.

         Wildcards are not allowed in file specifications on Kermit-40.



 March 1986                                                      Page    9
                           Kermit-40 Users Guide


     Binary files:

         To send files containing binary images, it is  necessary  to  use
     the SET BINARY ON command, (see 5.3.12) before carrying out the above
     instructions.  The  micro-kermit  must  be capable of doing eight bit
     quoting.  (See preface, 'Binary File Transfer')

           ___________________________________
     5.2   To receive files from micro-kermit.

     RECEIVE command                                                       |
                                                                           |
     Format:                                                               |
                                                                           |
         RECEIVE[ filename]                                                |

         This command switches  Kermit  into  receive  mode,  after  which
     Kermit-40 will  sit  and  wait  for the first valid packets to arrive
     from micro-kermit.   At  this  stage,  escape  and  return   to   the
     micro-kermit and  use  a  SEND file(s) command to start the transfer.
     If a filename is given to this command, then that will be used as the |
     received filename regardless of the name sent  by  micro-kermit.   If |
     however there  is  no  filename  given,  then  the  name  supplied by |
     micro-kermit will be used.  The filenames given by  micro-kermit  may |
     not be valid OS4000 names.  Provided Set Normal Off has not been set, |
     then this will not matter since Kermit-40 will hash any name given to |
     it into an acceptable name.  Firstly any non alpha-numeric characters
     will be  removed,  and if the result is longer than eight characters,
     then the name will be truncated to the last eight.  Secondly a period
     will be added to the front, and finally the /ADD  attribute  will  be
     added, which  implies that any existing file in the current catalogue
     with the same name will be appended to, (as in FTP).

         On completion  of  sending  files,  use  CONNECT  to  return   to
     Kermit-40 and  proceed with the next command, which could be to EXIT,
     SEND or RECEIVE more files.  If the transfer fails in  any  way,  and
     the process is not properly completed, it is possible that, on return
     to Kermit-40,  no  prompt  appears  on pressing <RETURN>.  This means
     that Kermit-40 is still in  Receive  mode,  and  pressing  control  Z
     <RETURN> should  allow  Kermit-40  to  be aborted, which must then be
     restarted before further attempts can be made.

     Binary files:

         To receive files containing binary images, it is necessary to use
     the SET BINARY ON command, (see 5.3.12) before carrying out the above
     instructions.  The micro-kermit must be capable of  doing  eight  bit
     quoting.  (See preface, 'Binary File Transfer')

           ____________________________
     5.3   To reset default parameters.

         There are a number of  parameters  which  start  with  a  default
     value.  For  many  cases  these  defaults  will  be  satisfactory  to
     inititiate and continue file transfer.   If,  however,  problems  are
     experienced, then  alteration  of some of these values may be needed.


 Page   10                                                      March 1986
                           Kermit-40 Users Guide


     For example,  if  your  micro-kermit  should  require   a   line-feed
     character to terminate input, instead of <RETURN>, then parameter EOL
     would need to be reset to ASCII code 10.

         When first trying to use Kermit-40 it may not be necessary to  be
     concerned about the SET command, except for binary file transfer, but
     if you  understand  communications  and think that some parameter may
     need to  be  reset,  then  reading  this  section  could  save   some
     frustration.  Obviously, if file transfers do fail to take place then
     it will  be neccessary to establish why and use this command to alter
     any suspect parameters.

     SET command

     Format:

         SET[ param][ value][ param[ value]...]

     For example:

         set binary on time 20

     will set binary file transfer to send or receive a LSB file, and tell
     micro-kermit to time me out after 20 seconds.

         This command allows tailoring of the communications  protocol  to
     your micro-kermit  and  hardware, as well as allowing setting of some
     useful switchable options such as DEBUG and BINARY.   Some  of  these
     communications parameters  are  set  during  an  initial  exchange of
     agreement which  takes  place  automatically  before  each   transfer
     begins, but  some  parameters  may need to be set by hand before even
     this initial exchange can take place, for example if EOL needs to  be
     set to  some  character  other than the default ASCII 13.  If this is
     wrong then the initial packets will  be  terminated  with  the  wrong
     end-of-line character,  and  may  therefore  not be recognised by the
     micro-kermit.  Although some parameters may be set by hand,  or  left
     at the  default  value  initially, they could later be overwritten by
     the agreed values provided by micro-kermit at the start of  transfer.
     The following  is  a list of the parameters set by the initial packet
     exchange.

         Received by Kermit-40 from micro-kermit:

         Maximum size of packet to send
         Period after which to time-out micro-kermit (** TIMEOUT)
         Number of pad characters to send (** PAD)
         Pad character to send (** CHAR)
         End-Of-line character to send (** EOL)
         Character to receive for control quoting
         Character to receive for 8 bit quoting
         Type of checksum to receive, (only one allowed in Kermit-40)
         Character to receive for repeat quoting                           |




 March 1986                                                      Page   11
                           Kermit-40 Users Guide


         Sent by Kermit-40 to micro-kermit:

         Maximum size of packet I receive
         Period after which Kermit-40 is to be timed out (** TIME)
         Number of pad characters to receive, (not required)
         Pad character to receive
         End-of-line character to receive
         Character I send for control quoting (** QUOTE)
         Character I send for 8 bit quoting (** 8BIT)
         Type of checksum I send, (only one done in Kermit-40)
         Character I send for repeat quoting (** REPEAT)                   |

     Those parameters which can be set in advance with the SET command are
     marked (** parameter-name)

     The parameters adjustable, and  their  functions  are  listed  below.
     They can  all  be  abbreviated  sensibly.  Further explanation may be
     found by reference to the KERMIT protocol manual.

         5.3.1   DEBUG (off/on)

             Switch debugging mode.  Whenever  Kermit-40  is  run  a  file
         called &KERMLOG  is opened.  This normally will contain a minimum
         of information logging the use of Kermit-40, such as the commands
         given and the result, success or failure.  However,  the  command
         SET DEBUG  ON,  will  cause  much  more data to be logged to this
         file, enabling failures  and  errors  to  be  tracked  down.   If
         &KERMLOG already exists it will be appended to.

         The additional details logged are as follows:

         *   All characters received and  sent,  which  will  include  all
             packets and any other spurious data which may arise.

         *   The results of decoding each packet received, giving  length,
             packet number, type and data buffer.

         *   The encoding details of  each  packet  sent,  giving  length,
             packet number,  type  and  data  buffer,  and also the packet
             itself.

         *   Changes of state within the  program  state  table  switcher,
             (see Kermit Protocol Guide, 5th ed, p17, 5.8)

         Default, Debug off

         5.3.2   EOL n

             SETs the packet end of  line  terminator  character  sent  to
         micro-kermit as ASCII value n (in decimal).

         Default, 13 (<RETURN>)




 Page   12                                                      March 1986
                           Kermit-40 Users Guide


         5.3.3   STX n

             SETs the start-of-packet  synchronising  character  to  ASCII
         value n  (in decimal).  Some micros or communications systems may
         respond incorrectly when the normal STX  character  is  sent,  so
         this enables  it  to be changed, (provided the same change is set
         on the micro-kermit.)

         Default, 1 (SOH)

         5.3.4   PAD n

             This will cause n CHAR characters  (see  below)  to  be  sent
         before each  packet.   These  padding  characters  are  sometimes
         required to give time for the micro-kermit, or the communications
         line, to 'turn-around' after each packet.  The  actual  character
         used is as defined by SET CHAR n .  (see below)

         Default, 0 (no characters sent)

         5.3.5   CHAR n

             This parameter defines the padding character  sent  when  PAD
         (above) is  set to n>0.  n is the ASCII value (in decimal) of the
         required character.

         Default, 0 (null)

         5.3.6   SEND n

             When sending files to micro-kermit, there is a  delay  period
         before the  first  packet is sent, to allow the user to return to
         micro-kermit to switch  to  receive  mode.   The  period  can  be
         altered with this command and is specified in seconds and must be
         greater than or equal to zero.

         Default, 15 seconds

         5.3.7   RETRYS n

             This defines the maximum number of times to retry  sending  a
         packet that  is  rejected by micro-kermit.  The number must be in
         the range 0 - 50 times.

         Default, 10 times

         5.3.8   TIME n

             This parameter, sent  out  at  initialisation,  requests  the
         number   of  seconds  after  which  micro-kermit  should  timeout
         Kermit-40.  It must be greater than or equal to one second.

         Default, 5 seconds



 March 1986                                                      Page   13
                           Kermit-40 Users Guide


         5.3.9   TIMEOUT n

             This specifies the period after which Kermit-40 will  timeout
         the micro-kermit  if  there  has  been  no  packet  received when
         expected.  It is given in seconds, and must be  greater  than  or
         equal to one second.

         Default, 10 seconds

         5.3.10   QUOTE n

             Control-quoting, when  sending  data  to   micro-kermit,   is
         normally  carried  out  using  the  ASCII  '#'  character.   This
         character will be inserted into sent  data  preceeding  any  byte
         which has  an  ASCII  value  less  than 32, and also preceeding a
         delete character,  hex  FF.   It  has  to  be  agreeable  to  the
         micro-kermit   and  will  be  checked  in  the  initial  exchange
         agreement.  The  character  can  be  altered  by   setting   this
         parameter to  a  new  ASCII  code  (in  decimal) for the required
         character.

         Default, 35 ('#')

         5.3.11   8BIT n

             Eight bit quoting is intended for use when transfering binary
         files, and is carried out normally with the '&' character.   This
         character will be inserted into the sent data preceeding any byte
         in which  the eigth bit is set to one.  It has to be agreeable to
         the micro-kermit and will be  checked  in  the  initial  exchange
         agreement.  In  this  way,  8  bit  bytes  can be transfered over
         7-bit-plus-parity asynchronous  lines.   The  character  can   be
         altered by  setting  this  parameter  to  a  new  ASCII  code (in
         decimal) for the required character.

         Default, 38 ('&')

         5.3.12   BINARY (off/on)

             This parameter must be switched on if transfer of a LSB  file
         is to  take  place.  When this is set then Kermit-40 will ask the
         micro-kermit to do eight bit quoting.  If  this  is  not  agreed,
         (not all  Kermits  can do this) then Kermit-40 will abort with an
         error message, and binary files cannot be transferred.

         Default, off (LST textfiles only)

         5.3.13   REPEAT                                                   |
                                                                           |
             Repeat quoting  is  used  when  agreed,   and   allows   data |
         compression by  expressing,  for  example, sequences of 4 or more |
         similar characters in terms of only three characters.  The  quote |
         character used  is  normally  the  '~',  and  must  be  agreed by |
         micro-kermit in the initial exchange  agreement.   The  character |


 Page   14                                                      March 1986
                           Kermit-40 Users Guide


         can be  altered by setting this parameter to a new ASCII code (in |
         decimal) for the required character.                              |
                                                                           |
         Default, 126 ('~')                                                |
                                                                           |
         5.3.14   NORMAL (on/off)                                          |
                                                                           |
             Normal mode  refers  to  the  conversion  of   filenames   to |
         'Normal-form'.  When  filenames  are  sent  from  micro-kermit to |
         Kermit-40, they are not always  likely  to  be  valid  names  for |
         OS4000.  Similarly,  when  sending  a  filename  to micro-kermit, |
         Kermit-40 does not know anything about the rules of filenames  on |
         that system.   Thus  the filenames will be hashed by Kermit-40 as |
         described under SEND and RECEIVE commands  described  previously, |
         providing NORMAL is set On.                                       |
                                                                           |
             If however, NORMAL is set Off, then no hashing will occur  at |
         all, and  whatever  micro-kermit  sends  for  filenames  will  be |
         offered to OS4000 for the Kermit-40  filenames.   Obviously  they |
         will be  rejected by OS4000 if not valid.  If the RECEIVE command |
         has been used with an  argument,  then  the  name  given  in  the |
         argument will be used anyway, regardless of whatever micro-kermit |
         sends.  When  micro-kermit  is receiving files from Kermit-40, it |
         will similarly have to be able to cope with the full OS4000 names |
         given in the Kermit-40 SEND command.                              |
             This option therefore allows full directory structures to  be |
         used if required.                                                 |
                                                                           |
         Default, on                                                       |

           __________________________________________
     5.4   To display the settings of SET parameters.

     SHOW

         The SHOW command displays the current settings of the  parameters
     as defined by SET, or as over-written by the initialisation sequence.




















 March 1986                                                      Page   15
                           Kermit-40 Users Guide


     eg:                                                                   |
                                                                           |
     Kermit-40> show                                                       |
                                                                           |
     KERMIT file transfer utility, Version 40/3.2 for GEC 4000             |
      Status of SET parameters-                                            |
      Debug      is set to        OFF                                      |
      Eol        is set to        13                                       |
      Stx        is set to         1                                       |
      Pad        is set to         0                                       |
      Char       is set to         0                                       |
      Send       is set to        15                                       |
      Retrys     is set to        10                                       |
      Time       is set to         5                                       |
      Timeout    is set to        10                                       |
      Quote      is set to        35                                       |
      8bit       is set to        38                                       |
      Binary     is set to        OFF                                      |
      Repeat     is set to       126                                       |
      Normal     is set to        ON                                       |
                                                                           |
           ____________________________________________
     5.5   To switch Kermit-40 into remote Server mode.                    |
                                                                           |
     SERVER                                                                |
                                                                           |
         If this command is given then Kermit-40 will immediately go  into |
     remote server mode, after which it will wait in 'Receive-Idle' state, |
     for commands  from the micro-kermit.  The message shown below will be |
     displayed:                                                            |
                                                                           |
     Kermit-40:  Server running, Now type local escape sequence-           |
                                                                           |
         The Server commands  supported  which  may  be  issued  from  the |
     micro-kermit, assuming  it  is capable of giving commands to a remote |
     server, are:                                                          |
                                                                           |
     SEND                                                                  |
         Files will be sent from the micro-kermit to Kermit-40, the normal |
     rules for Kermit-40 RECEIVE will apply.                               |
                                                                           |
     GET                                                                   |
                                                                           |
         Files will be sent as requested from Kermit-40  to  micro-kermit, |
     and the normal rules for Kermit-40 SEND will apply.                   |
                                                                           |
     FINISH                                                                |
                                                                           |
         Kermit-40 Server mode will close down, Kermit-40  will  still  be |
     active and  will  be awaiting input to it's usual prompt, Kermit-40>. |
     Note that this is  not  standard  Kermit  practice,  since  Kermit-40 |
     should close  down completely.  However, especially since this Server |
     recognises no command to  change  Kermit-40  SET  parameters,  it  is |
     useful to  be  able  to come back to this Kermit to change parameters |
     and then continue server mode again.  See BYE below.                  |


 Page   16                                                      March 1986
                           Kermit-40 Users Guide


                                                                           |
     BYE, or LOGOUT                                                        |
                                                                           |
         Kermit-40 will close down completely.  It  is  not  possible  nor |
     desirable to  logout  a  user under GEC OS4000, therefore there is no |
                                                    _______________
     further effect of this command.  The user will stay logged in.        |

           _________________________________________________
     5.6   To obtain on-line help on the Kermit-40 commands.

     HELP

     Format:

         HELP[ command command....]

         Typing HELP alone will display the version  number  of  Kermit-40
     and the  commands  available.   Typing  HELP 'command' will give full
     information on that command.

           _______________________
     5.7   To exit from Kermit-40.

     EXIT

         Type EXIT to leave Kermit-40 when transfers are finished.
































 March 1986                                                      Page   17
                           Kermit-40 Users Guide




     ___________________________
 6   Examples of using Kermit-40

       __________________________________
 6.1   Example- Kermit-40/IBM PC (Telios)

     Below is given an example of file transfers between Kermit-40 and the
 IBM PC, using TELIOS (Genasys Corporation) in Kermit emulation mode.   In
 this example the PC is connected to the GEC via a RAL PAD line.

 Note- Comments are (in parenthesis)

    ______
 A: telios                  (Invoke Telios on the PC, from logged-on disc A:)

   _________
 > baud 4800                (set speed, full duplex, and Kermit protocol)
   ________
 > echo off
   _______________
 > protocol kermit
   ________
 > <RETURN>            (carriage return causes Telios to resume CONNECT mode)
 ________
 <RETURN>              (carriage return awakes PAD)
 * RAL Atlas PAD RLCG (Vn 2.1R) DTE=1106 line 9 speed 4800

     ____________
 PAD>controlchars      (allow control characters through the pad)

     _________
 PAD>call rlgb         (logon to RLGB)
 ****  This is the Rutherford GEC 4090 - RLGB  ****

 OS4000+Rlix V25 RAL Atlas
 Logging in
      _____
 user notu2
 password

 ID last used Wednesday, 30 January 1985 11:24
 Started - Wed 30 Jan 1985 11:27:39
 ready
 ______________
 raresys.kermit       (start Kermit-40)
 KERMIT file transfer utility, Version 40/3.2 for GEC 4000 by M J Loach, RAL.
 Kermit-Copyright Columbia University Centre for Computing Activities, 1986

            ________
 Kermit-40> help set   (use help command to check if parameters need setting)

                             SET COMMAND
                             ***********

   (SET) allows certain parameters to be switched on and off, or set to a
   value. The ones available at present are-    (s-on/off, n-value)
   DEBUG s- If on, debugging information is logged to .KERMLOG, default off
   EOL n-   set END-OF-LINE character, to ascii value n, default 13(CR)
   STX n-   set start of packet text sync char to ascii n, default 1
   PAD n-   set number of pad characters to preceed each packet, default 0
   CHAR n-  set pad character to be ascii n, default 0 (null)
   SEND n-  set delay before first SEND packet to n secs, default 15
   RETRYS n-set maximum number of sending retries before abort,default 10
   TIME n-  set number of seconds before micro-kermit times me out, def 5
   TIMEOUT n- set number of seconds for Kermit-40 timeout, default 10


 Page   18                                                      March 1986
                           Kermit-40 Users Guide


   QUOTE n- set the ASCII value of the character I send for quoting,def 35
   8BIT n-  set ASCII value of the character I send for 8bit quoting. (38)
   BINARY s-If on, LSB files are sent and received, via 8bit quote. (off)
   REPEAT n-set ASCII value of the character I send for repeat quote.(126)
   NORMAL s-If on, filenames are converted to a 'normal form', default on

            ____________
 Kermit-40> set debug on  ( decide to set debugging mode, into file &kermlog)
            _____________
 Kermit-40> send .kermdoc   ( going to send .kermdoc to the PC)
 _______
 (alt-H)               (get back to PC command level)
   ____________
 > pcapture k.k        (tell PC to capture the file about to be sent to it,)
  Recvd #00001         (as k.k . 'P'rotocol 'Capture' refers to Kermit, as)
  Recvd #00002         (chosen at the start, above)
  ......
  Recvd #00212         (last packet received)
 #7YU                  (last packet from Kermit-40, superfluous)
           _
 Kermit-40>q           (quit Kermit-40)
 ready                 (GEC prompt)

 _______
 (alt-H)               (return to PC Telios command mode)
   ________
 > type k.k            (type file captured, to see if OK.)
  .......
 ________
 <RETURN>              (return to CONNECT mode)
 ready                 (GEC prompt)
 ______________
 raresys.kermit
 KERMIT file transfer utility, Version 40/3.2 for GEC 4000 by M J Loach, RAL.
 Kermit-Copyright Columbia University Centre for Computing Activities, 1986

            ___
 Kermit-40> rec        (switch kermit-40 to receive a file from the PC)
 _______
 (alt-H)
  ______________
 >psend demo.fil       (ask PC to send demo.fil from disc A: to GEC)
  Sent #00001          (sends ok)
  Sent #00002
  ......
  Sent #00031
            _
 Kermit-40> q          (finished)
 ready                 (GEC prompt)
 _____________
 type .demofil         (check file is on GEC)
  .......
 ready              (GEC prompt)
 __
 lo                 (logout)
 CPU used: 1 ieu, Elapsed: 2 mins, IO: 772 units, Breaks: 20
 Budgets: this period = 15.400 AUs, used = 0.010 AUs, left = 14.303 AUs
 User NOTU2 terminal  14 logged out  Wed 30 Jan 1985 11:26:47


 PAD>clear

 *** Cleared








 March 1986                                                      Page   19
                           Kermit-40 Users Guide



       _____________________________________
 6.2   Example- Kermit-40/IBM PC (Kermit-MS)

     Below is given an example of file transfers between Kermit-40 and the
 IBM PC, using Kermit-MS.  In this example the PC is connected to the  GEC
 via a RAL PAD line.

 Note- Comments are (in parenthesis)

    ______
 C> kermit      (invoke kermit on PC, from logged-on disc C:)

 IBM-PC Kermit-MS V2.27
 Type ? for help

            _______________
 Kermit-MS> set parity even      (even parity for GEC MUM)
            _______
 Kermit-MS> connect

 [Connecting to host, type Control-] C to return to PC]

 ________
 <RETURN>      (awake PAD at RAL)
 * RAL Atlas PAD RLCG (Vn 2.1R) DTE=1106 line 9 speed 4800

     ____________
 PAD>controlchars      (allow control characters through the pad)

     _________
 PAD>call rlgb         (logon to RLGB)
 ****  This is the Rutherford GEC 4090 - RLGB  ****

 OS4000+Rlix V25 RAL Atlas
 Logging in
      _____
 user notu2
 password

 ID last used Wednesday, 30 January 1985 12:19
 Started - Wed 30 Jan 1985 17:27:01
 ready
 ______________
 raresys.kermit            (start Kermit-40)
 KERMIT file transfer utility, Version 40/3.2 for GEC 4000 by M J Loach, RAL.
 Kermit-Copyright Columbia University Centre for Computing Activities, 1986
                           (firstly receive a binary file from the PC)
            _____________
 Kermit-40> set binary on
            _______
 Kermit-40> receive        (receive a LSB file into the current catalogue)
 ____________
 <Control-]C>              (return to PC)

            ______________
 Kermit-MS> send a:char256 (tell it to send a file from disc A)
 (now the screen will show the following display:)











 Page   20                                                      March 1986
                           Kermit-40 Users Guide



             File name :
    KBytes transferred :

             Sending   : In progress

     Number of packets : 0
     Number of retries : 0
            Last error : None
          Last warning : None




 (this display updates as the transfer takes place, and will appear thus,
 when finished:)

             File name : CHAR256
    KBytes transferred : 0
   Percent transferred : 100%
             Sending   : Completed

     Number of packets : 12
     Number of retries : 0
            Last error : None
          Last warning : None




            _______
 Kermit-MS> connect                (now go back and send file back to PC)

 [Connecting to host, type Control-] C to return to PC]

 ________
 <RETURN>                          (get Kermit prompt on GEC)
            _____________
 Kermit-40> send .char256          (send the LSB file back to the PC again)
 ____________
 <Control-]C>                      (return to PC)

            ___
 Kermit-MS> rec



             File name :
    KBytes transferred :

             Receiving : In progress

     Number of packets : 0
     Number of retries : 0
            Last error : None
          Last warning : None

 (this display updates as the transfer takes place, and will appear thus,
 when finished:)


 March 1986                                                      Page   21
                           Kermit-40 Users Guide




             File name : CHAR256
    KBytes transferred : 0

             Receiving : Completed

     Number of packets : 13
     Number of retries : 0
            Last error : None
          Last warning : None




            _______
 Kermit-MS> connect

 [Connecting to host, type Control-] C to return to PC]

 ________
 <RETURN>            (get Kermit prompt on GEC)
            ____
 Kermit-40> exit     (finished)
 ready               (GEC prompt)
 __
 lo                  (logout)
 CPU used: 1 ieu, Elapsed: 4 mins, IO: 1043 units, Breaks: 20
 Budgets: this period = 15.400 AUs, used = 0.010 AUs, left = 14.303 AUs
 User NOTU2 terminal  14 logged out  Wed 30 Jan 1985 17:35:15

 PAD>clear

 *** Cleared


























 Page   22                                                      March 1986
                           Kermit-40 Users Guide



       _______________________________________
 6.3   Example- Kermit-40/ VAX/VMS (Kermit-32)

     Below is given an example of file transfers between Kermit-40 and the
 VAX 11/750, using Kermit-32.  Kermit-32 is run from  terminal  NVA1:,  to
 which has  been  allocated terminal TTA2:  .  A connection has been wired
 from a PACX line connected to TTA2:  , to another  PACX  line  which  has
 already been connected to, and logged in to RLGB.

 ie:

 NVA1 to Kermit-32 to TTA2 to PACX to PACX to RLGB

     It is unlikely that anyone would want to  use  this  method  of  file
 transfer between  VAX/GEC,  especially  since  transfer  via  SERCNET  is
 easier.  However, it is a  useful  example  showing  the  versatility  of
 Kermit.

 Note- Comments are (in parenthesis)

 (logging into VAX...)

 Central Computing Division Vax 11/750

           ______
 Username: Anyone

 Password:


                 Welcome to RLVE running VMS V3.7

 If you are connected to this Vax via PACX please hit the PACX key
 after you have logged off.
   ________
 $ all tta2                            (allot another port to connect to GEC)

     TTA2: allocated
   ________________________
 $ set term tta2/speed=4800            (set its speed accordingly)
   ______
 $ kermit                              (start Kermit)

 VMS Kermit-32 version 3.0.051
 Default terminal for transfers is:  NVA1:
           _____________
 Kermit-32>set line tta2               (tell kermit which port)
           _______________
 Kermit-32>set parity even             (set its parity)
           ______________
 Kermit-32>local host dir              (DIR command to VAX)

 Directory DUA0:[ANYONE]

 0R.DOC;1            COM.DOC;1           CONTROL.EXE;1       CONTROL.FOR;1
 CONTROL.OBJ;1       FILE.TXT;4          FLY.DOC;1           INITB.;1
 INITK.;3            INITK.;2            INITK.;1            KERMIT.DIR;1
 LOGIN.COM;3         MAIL.MAI;1          MAILMAI.;1          TEST.FDL;1
 VER.DOC;1

 Total of 17 files.


 March 1986                                                      Page   23
                           Kermit-40 Users Guide


           _______
 Kermit-32>connect                     (connect to GEC)

 [RLVED::Connecting to  TTA2:.  Type ^]C to return to VAX/VMS Kermit-32]

 ________
 <RETURN>                              (get prompt, already logged in)
 ready                                 (GEC prompt)
 ______________
 raresys.kermit                        (run Kermit-40)
 KERMIT file transfer utility, Version 40/3.2 for GEC 4000 by M J Loach, RAL.
 Kermit-Copyright Columbia University Centre for Computing Activities, 1986

            ___
 Kermit-40> rec                        (prepare to receive file from VAX)
 ____________
 <Control-]C>                          (return to VAX)

 [RLVED::Returning to VAX/VMS Kermit-32]

           ____________
 Kermit-32>send ver.doc                (ask VAX to send file to GEC)

 Sending: DUA0:[ANYONE]VER.DOC;1 as VER.DOC (this is displayed when sending)

 (when finished the word OK is added thus:)

 Sending: DUA0:[ANYONE]VER.DOC;1 as VER.DOC[OK]
           _______
 Kermit-32>connect                     (return to GEC)

 [RLVED::Connecting to  TTA2:.  Type ^]C to return to VAX/VMS Kermit-32]

 ________
 <RETURN>
            __________
 Kermit-40> send .inik                 (now send a file to VAX)
 ____________
 <Control-]C>

 [RLVED::Returning to VAX/VMS Kermit-32]

           ___
 Kermit-32>rec                         (switch VAX to receive)
 Kermit-40: Cannot open file: .INIK        (message from GEC Kermit)

           _______
 Kermit-32>connect                     (return and try again)

 [RLVED::Connecting to  TTA3:.  Type ^]C to return to VAX/VMS Kermit-32]

 ________
 <RETURN>
            ___________
 Kermit-40> send .initk
 ____________
 <Control-]C>

 [RLVED::Returning to VAX/VMS Kermit-32]

           ___
 Kermit-32>rec

 Receiving: INITK  as DUA0:[ANYONE]INITK.;4   (this time transfer starts ok)

 (display is as below when finished:)

 Receiving: INITK  as DUA0:[ANYONE]INITK.;4[OK]
           ____
 Kermit-32>quit
 $


 Page   24                                                      March 1986
                           Kermit-40 Users Guide


     _______________________________
 7   What to do when things go wrong

       ______________________________________
 7.1   Failure to be able to Connect to host.

     Check the following:

     *   micro-kermit set for even parity
     *   micro-kermit set for correct baud rate
     *   communications medium, eg PAD, set to  allow  control  characters
         through
     *   micro-kermit set to use correct port on micro
     *   cable correct to link micro to comms port
     *   micro-kermit set to operate in full duplex(no-echo)

       ______________________________________
 7.2   Failure of the transfer of the file(s)

     There are two ways in which failure may be indicated.



         1.  Transfer completes but on inspection the file  has  not  been
             transferred correctly

         2.  Transfer aborts, or just halts, with  or  without  a  failure
             message


     In the first instance a rare combination of errors  has  led  to  the
 error checksum  being  corrupted  and  then corrupted back to the correct
 value for the corrupted packet.  This has then been accepted as  a  valid
 packet.  The  chances  of  this sort of problem occuring are small unless
 there are a lot of short bursts of corruption on  the  link,  leading  to
 many packets  being repeated.  Trying the transfer again may well lead to
 a successful result.

     In the second case it is worthwhile trying a second time to make sure
 a spurious error did not occur.  If problems are encountered  then  check
 the following:


     *   All the possible causes in 7.1, above
     *   Check the SET parameters, particularly if the failure is  at  the
         start, both on Kermit-40 and on micro-kermit (see 5.3)

     Note that if you return to Kermit-40 to find it is no longer running,
 but you have a  GEC  OS  prompt  instead,  then  Kermit-40  has  probably
 crashed.  If  so,  please  report with as much information as possible to |
 NSIN12 @ UK.AC.RL.GK








 March 1986                                                      Page   25
                           Kermit-40 Users Guide


     __________
 8   Appendix A

                     ____________________________________
                     Error messages and their explanation


 _________________________
 There is a checksum error

     This is written to the  log  file  each  time  a  checksum  error  is
     encountered in  the  incoming  packets.   It  is a warning only and a
     negative-ackknowledgement will be sent to the  micro-kermit  until  a
     correct packet  is  received  or  the  maximum  number  of retries is
     exceeded.

 _________________________________
 File being opened for sending is:

     This gives the name of the next file  obtained  from  the  file  list
     given on the send command.

 __________________
 Closing input file

     This is output when the currently sent file is completed.

 ___________________________
 looking for next file......

     This is output after the above message and indicates  that  Kermit-40
     is looking for the next filename from the SEND filelist.

 ____________
 New file is-

     This gives the name of the next file obtained from the filelist given
     on the SEND command.

 ____________
 Send command

     This indicates that the SEND command has been given

 _______________
 Receive command

     This indicates that the RECEIVE command has been given

















 Page   26                                                      March 1986
                           Kermit-40 Users Guide




 ______________
 Receive failed

     This means  that  receiving  a  file  has  failed.   This  could   be
     accompanied by any of the following messages-


 Eight bit quoting not agreed.

 Number of retries exceeded.

 Packet number is out of sequence.

 Failed to connect to file.

 File is wrong type, compared to existing file, ie not LSB or not LST.

 _____
 done.

     Output on completion of the SEND or RECEIVE command.

 ___________
 Send failed

     This means that sending a file has failed.  This could happen due  to
     any of the reasons given under Receive Failed (above).

 _____________________________________________
 File already exists with different attributes

     An attempt has been made to  receive  a  file  which  already  exists
     having a different type, eg receiving a binary file when a CAT or LST
     file exists with the same name.

 __________________________________________________________
 Kermit aborting with the following error from remote host:

     This accompanies a message which has been received from  micro-kermit
     in an error packet.

 ______________
 Cannot create:

     Receiving a file has been aborted because an attempt  to  connect  to
     the file  specified  for  creation failed.  Could be due to trying to
     receive to an existing LSB file (/ADD attribute cannot be  used  with
     LSB).

 ___________________________
 Cannot open file:(binary?):

     On receiving a text file a LSB file has been found to  already  exist
     with the same name, or, on sending a text file, the file specified is
     in fact a LSB file.

 _____________________________
 Cannot open file:(textfile?):

     On receiving a binary file a LST file has been found to already exist


 March 1986                                                      Page   27
                           Kermit-40 Users Guide


     with the same name, or, on sending a binary file, the file  specified
     is in fact a LST file.

 ___________________________
 Cannot open file:(not LS?):

     On receiving a file a non logical sequencial file has been  found  to
     already exist  with  the  same  name, or, on sending a file, the file
     specified is in fact a non logical sequential file  (eg,  attempt  to
     transfer a catalogue).

 _______________________
 DM Error, RA= @hexvalue                                                   |
                                                                           |
     This gives the Data management error code associated with  attempting |
     to connect  a  filename  to  a  stream(DMCONNECT),  and is written to |
     &KERMLOG.                                                             |

 __________
 Sending as

     Kermit-40 takes the catalogue name of a  file  and  removes  all  the
     catalogue   structure,  leaving  just  the  filename  without  a  '.'
     character, to give as the name for the file to be sent.   This  shows
     the name which has been constructed.

 ____________
 Receiving as                                                              |
                                                                           |
     This shows the name being given to the received  file  under  OS4000, |
     which   will  normally  be  as  hashed  from  the  name  supplied  by |
     micro-kermit, but  could  be  as  specified  by  a  RECEIVE  filename |
     command.                                                              |

 ______________________________________
 Timeout retries exceeded, press return

     This message will appear on the terminal stream  when  Kermit-40  has
     aborted due  to  timeout retries exceeding the maximum.  This is most
     likely to be due to a failure in the communications between  the  two
     Kermits.  In  this  situation, the timeouts occured due to no records
     being received by Kermit-40 from the terminal stream.  The result  is
     that there is still an outstanding GET which must be satisfied before
     Kermit-40 can  continue  with  any more commands successfully.  Hence
     the reason to have to  press  return  once  before  the  prompt  will
     appear.  In  most  situations  the  user  will  probably not see this
     message on the screen, and will have pressed return anyway to  get  a
     Kermit-40 prompt.

 __________________________________
 Too many retries, transfer aborted

     This means that Kermit-40 has given up retrying to send or receive  a
     packet which  is  either  corrupted  in transmission or incorrect for
     some reason.   It  is  most  likely  due  to   a   failure   in   the
     communications between the two Kermits.

 _____________________________________________________
 8 bit quoting not agreed, so can't do binary transfer

     The micro-kermit rejected  the  request  to  do  8  bit  quoting,  so


 Page   28                                                      March 1986
                           Kermit-40 Users Guide


     Kermit-40   will  not  be  able  to  transfer  a  binary  file.   The
     micro-kermit presumeably has no eight bit quote facility.

 ______________
 Kermit aborted

     This message is output when control-Z is used to jump out of  Kermit.

 _______________
 Invalid command

     A command typed in to the Kermit-40 prompt was un-recognised.

 _________________
 Excess parameters

     More than the allowed number of parameters have been  typed  after  a
     command.

 _________________
 Invalid parameter

     A parameter typed after a command is not  recognised  or  is  missing
     when required.

 ______________
 No information

     Output by the Help command if the help requested is not available, ie
     the command given does not match any Kermit-40 command.

 ______________________
 Parameter out of range

     A parameter given to the SET command is invalid,  eg  a  negative  or
     zero timeout, or an excessively large number of permitted retries.

 ____________________________
 Unimplemented server command                                              |
                                                                           |
     In Server  mode,  an  unsupported  command  has  been  received  from |
     micro-kermit.  The  command  subset  allowed currently is, GET, SEND, |
     FINISH, BYE and LOGOUT.                                               |
                                                                           |
 ________________________________
 Taking commands from With stream                                          |
                                                                           |
     An argument has been supplied for the WITH stream for this  run,  and |
     Kermit-40 is reading commands from this file.                         |
                                                                           |
 ___________________
 End of command file                                                       |
                                                                           |
     Kermit-40 has read all the commands from the WITH stream, and is  now |
     expecting terminal commands again.                                    |










 March 1986                                                      Page   29
                           Kermit-40 Users Guide


                                  References

 1. Kermit Protocol Manual, Fifth edition, Frank da Cruz, Columbia University
 Centre for Computing Activities, New York 10027, 3 April 1984.

 2. Kermit Users Guide, Fifth edition, Rev 1, Frank da Cruz, Columbia
 University Centre for Computing Activities, New York 10027, 27 July 1984.

 3. Access to Kermit Distribution at Lancaster, M J Loach, October 1985.      |















































 Page   30                                                      March 1986