Description of Socket-Interface-Protocol Rev.2
----------------------------------------------

Mark Wahl, DL4YBG
Created: 26.11.94
Last Update: 13.04.96


0. General Layout
-----------------

Indicator (1 Byte)
Channel   (2 Byte)
Usernr    (2 Byte)
Length    (2 Byte)
Data      (Length Bytes)

1. Commands
-----------

1.1 Activate Program
--------------------
(PR->Program)
On the specified channel the linked program (defined by used socket)
shall be activated (the interface will be opened).
If channel is 0, the activation is started from the operator console
instead of a packet channel.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_SIMPLE + (strlen(callsign) + 1)
Command   (4 Byte)
  CMD_ACTIVATE
Callsign  ((strlen(callsign) + 1) Byte)
  char callsign[]


1.2 Deactivate Program
----------------------
(PR->Program)
On the specified channel the linked program (defined by used socket)
shall be deactivated (the interface will be closed).

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE
Command   (4 Byte)
  CMD_DEACTIVATE


1.3 Connect
-----------
(Program->PR)
A free channel shall be used to build up a connection. QRG, Sourcecall, 
Destinationcall and a connection-build-up-timeout must be specified.
The connection will be build up using xconnect-feature, therefore no
digipeaterpath is allowed.
The user 'usernr' will be informed about the result of the connect,
successful or not.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_CONNECT + (strlen(sourcecall) + 1) + (strlen(destcall) + 1)
Command   (4 Byte)
  CMD_CONNECT
Timeout   (4 Byte)
  int timeout
Qrg       (20 Byte)
  char qrg[20]
Sourcecall (strlen(sourcecall) + 1)
  char sourcecall[]
Destcall (strlen(destcall) + 1)
  char destcall[]


1.4 Disconnect
--------------
(Program->PR)
The connection on the specified channel shall be disconnected.

Indicator (2 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE
Command   (4 Byte)
  CMD_DISCONNECT


1.5 Finish Program
------------------
(Program->PR)
If the program was started directly (using special SSID), the connection
will be disconnected.
Otherwise a reconnection to the last used command processor will occur
(reconnect to terminal/node-software).

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE
Command   (4 Byte)
  CMD_FINISH


1.6 Channel Status
------------------
(PR->Program)
If the number of frames in the TX-buffer (Program and TNC) has changed
on a channel linked to a program, a channel status message with the
new number of frames in TX-buffer will be sent.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_CSTATUS
Command   (4 Byte)
  CMD_CSTATUS
Number of frames in TX-buffer (4 Bytes)
  int snd_frames
  

1.7 Blocking
------------
(Program->PR, PR->Program)
If blocking is received, the sending side has reached maximum byte count
and is waiting for an unblocking message. Otherwise no data will be
transmitted.
This is a simple handshake to avoid an overrun of the socket.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_SIMPLE
Command   (4 Byte)
  CMD_BLOCK


1.8 Unblocking
--------------
(Program->PR, PR->Program)
unblock restarts the transmitter on the other side of the interface.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_SIMPLE
Command   (1 Byte)
  CMD_UNBLOCK


1.9 Sort new mail
-----------------
(PR->DPBox)
A mail was collected from monitor or during connect with a mailbox.
Pattern is the filename of the used file, Rcall is the callsign of
the mailbox where this file was fetched (or an empty string). Not
used for S&F connects, only for monitoring features.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE + (strlen(pattern_) + 1) + (strlen(rcall) + 1)
Command   (4 Byte)
  CMD_SORT_NEW_MAIL
Pattern   ((strlen(pattern_) + 1) Bytes)
  char pattern_[]
Rcall     ((strlen(rcall) + 1) Bytes)
  char rcall[]


1.10 SF Rx EMT
--------------
(PR->DPBox)
A mail for folder 'E', 'M' or 'T' was received. These mails consist only
of one line. This line will be sent directly in Eingabe. Not used for
S&F connects, only for monitoring features.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE + (strlen(eingabe_) + 1)
Command   (4 Byte)
  CMD_SF_RX_EMT
Eingabe   ((strlen(eingabe_) + 1) Bytes)
  char eingabe_[]


1.11 Connect for Store and Forward
----------------------------------
(DPBox->PR)
A free channel shall be used to build up a connection for Store and
Forward. Sourcecall, Destinationcall and a connection-build-up-timeout
must be specified.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_BOXPBOXSF + (strlen(sourcecall) + 1) + (strlen(destcall) + 1)
Command   (4 Byte)
  CMD_BOXPBOXSF
Timeout   (4 Byte)
  int timeout
Sourcecall (strlen(sourcecall) + 1)
  char sourcecall[]
Destcall (strlen(destcall) + 1)
  char destcall[]


1.12 Disconnect
---------------
(DPBox->PR)
The connection on the specified channel shall be disconnected.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE
Command   (4 Byte)
  CMD_BOXPRDISC


1.13 Abort Store and Forward
----------------------------
(DPBox->PR)
Store and Forward shall be cancelled. If Immediate is not 0, outstanding
TX-Packet must be cancelled, too.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (4 Byte)
  LEN_BOXPABORTSF
Command   (4 Byte)
  CMD_BOXPABORTSF
Immediate (4 Byte)
  int immediate


1.14 Abort Routing
------------------
(PR->DPBox)
A Connect command for Store and Forward sent by DPBox (CMD_BOXPBOXSF) was
not successful.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_SIMPLE + (strlen(callsign) + 1)
Command   (4 Byte)
  CMD_ABORT_ROUTING
Callsign  ((strlen(callsign) + 1) Byte)
  char callsign[]


1.15 Start Store and Forward
----------------------------
(PR->DPBox)
A Connect command for Store and Forward sent by DPBox (CMD_BOXPBOXSF) was
successful and S&F can begin.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_SIMPLE + (strlen(callsign) + 1)
Command   (4 Byte)
  CMD_START_SF
Callsign  ((strlen(callsign) + 1) Byte)
  char callsign[]


1.16 Finish Program
-------------------
(PR->Program)
The Program connected to the socket shall terminate the execution.
This is used to kill daemon-processes.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_SIMPLE
Command   (4 Byte)
  CMD_FINISH_PRG


1.17 Activation Response
------------------------
(Program->PR)
If a program was activated via CMD_ACTIVATE or CMD_START_SF, the resulting
usernr will be returned in this message. If the usernumber is equal 0,
then the activation was not successful.
In the response string additional information about the activation can
be transferred.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE + (strlen(response) + 1)
Command   (4 Byte)
  CMD_FINISH_PRG
Response  ((strlen(response) + 1) Byte)
  char response[]


1.18 AutoBIN-File to Box
------------------------
(PR->Program)
On the current channel a file was received with AutoBIN-protocol.
Erase defines if the file shall be deleted afterwards, error indicates
a wrong CRC-checksum and buffer contains the filename of the file.
No more supported by DPBOX, DPBOX handles AutoBIN itself.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_ABINFILETOBOX + (strlen(buffer) + 1)
Command   (4 Byte)
  CMD_ABINFILETOBOX
Erase     (4 Byte)
  int erase
Error     (4 Byte)
  int error
Buffer    ((strlen(buffer) + 1) Byte)
  char buffer[]  
  

1.19 Huffman Status
-------------------
(PR->Program) (Program->PR)
If huffman coding is enabled or disabled this message will inform the other
side about the new status. 1 means huffman coding is active, 0 means
inactive. Huffman encoding/decoding has to be done by PR.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_HUFFSTAT
Command   (4 Byte)
  CMD_HUFFSTAT
Huffstat  (4 Byte)
  int huffstat
  

1.20 Frequency Information
--------------------------
(PR->Program)
With this message all frequencies handled by the PR-program are sent to
the program. This information is used to find the right interface for
S&F by DPBox.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_QRGINFO
Command   (4 Byte)
  CMD_QRGINFO
Frequency  (220 Byte)
  char qrg[MAXQRGS+1][20] (MAXQRGS = 10)
  

1.21 Bulletin-ID query and answer
---------------------------------
(PR->DPBox)(DPBox->PR)
With this message the program can query if a mail is already available
in the DPBox by checking the bulletin ID. DPBox will answer in 'Found'
(0: not found, 1: found) and will return the bullid, too. Not used for
S&F connects, only for monitoring features and similar.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_BULLID
Command   (4 Byte)
  CMD_BULLID
Found     (4 Byte)
  int found
Bullid    (13 Byte)
  char bullid[BULLIDLEN+1] (BULLIDLEN = 12)
 

1.22 Start AutoBIN-receive
--------------------------
(DPBox->PR)
This message instructs TNT to prepare AutoBIN reception on the current
channel. The filename of the file to open will be given as parameter
(null-terminated string in buffer).
No more supported by DPBOX, DPBOX handles AutoBIN itself.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE + (strlen(buffer) + 1)
Command   (4 Byte)
  CMD_STARTABIN
Buffer    ((strlen(buffer) + 1) Byte)
  char buffer[]  
  

1.23 Update Box-timeout
--------------------------
(PR->DPBox)
During AutoBIN-receive TNT informs DPBox by this message that the user is
still active.
No more supported by DPBOX.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE
Command   (4 Byte)
  CMD_BOXTOUCH


1.24 Set Read/write Mode
------------------------
(DPBox->PR)
This message informs TNT if during a boxconnect the AutoBIN-header shall be
analysed (rwmode = 0) or not (rwmode = 1). 
No more supported by DPBOX, DPBOX handles AutoBIN itself.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SETRWMODE
Command   (4 Byte)
  CMD_SETRWMODE
Rwmode    (4 Byte)
  int rwmode
  

1.25 Box Is Busy
----------------
(DPBox->PR)
This message informs TNT if DPBox is busy and connects shall be rejected.
(boxisbusy = 0, connects allowed; boxisbusy = 1, no connects allowed)

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_BOXISBUSY
Command   (4 Byte)
  CMD_BOXISBUSY
Boxisbusy (4 Byte)
  int boxisbusy

  
1.26 Start Box Broadcast
------------------------
(DPBox->PR)
This message instructs TNT to start a broadcast transmission of a file.
The broadcast-header is contained in a file, the filename of this file is
stored in buffer.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_SIMPLE + (strlen(buffer) + 1)
Command   (4 Byte)
  CMD_STARTBOXBC
Buffer    ((strlen(buffer) + 1) Byte)
  char buffer[]  


1.27 Broadcast Callback
-----------------------
(PR->DPBox)
If the broadcast transmission of a file is finished, DPBox will be informed
by this message. The file is identified by the file_id contained in the
message.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_BCCALLBACK
Command   (4 Byte)
  CMD_BCCALLBACK
File_id   (4 Byte)
  long file_id


1.28 Set Unproto Destination
----------------------------
(DPBox->PR)
This message sets the unproto destination for the following unproto data.
The destination is stored independently for every interface.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  LEN_SETUNPROTO + (strlen(buffer) + 1)
Command   (4 Byte)
  CMD_SETUNPROTO
Qrg       (20 Byte)
  char qrg[20]
Address   ((strlen(address) + 1) Byte)
  char address[]  


1.29 Connect Not Successful
---------------------------
(PR->Program)
A connect, initiated by user 'usernr' was not successful.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE
Command   (4 Byte)
  CMD_NOSUCCESSCON


1.30 Connect Successful
-----------------------
(PR->Program)
A connect, initiated by user 'usernr' was successful and the link between
the two connects shall be established. The channel of the new connection is
contained in channel.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE + (strlen(callsign) + 1)
Command   (4 Byte)
  CMD_SUCCESSCON
Callsign  ((strlen(callsign) + 1) Byte)
  char callsign[]


1.31 TNT-Command
----------------
(Program->PR)
This command contains a command string, which shall be parsed and executed
by the TNT command processor. 'channel' is used as channel used for the
command. 'usernr' is the user, which must be informed about the result.
Only used in DPBOX for the TNTCOMM command.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE + (strlen(buffer) + 1)
Command   (4 Byte)
  CMD_TNTCOMMAND
Buffer    ((strlen(buffer) + 1) Byte)
  char buffer[]  


1.32 TNT-Response
-----------------
(PR->Program)
This message contains the response to the command given by CMD_TNTCOMMAND
(1.31 TNT-Command). 'follows' indicates, if other responses to the command
will follow, 'follows' == 0 indicates the last response.
'channel' is the given channel for the command and 'usernr' is the user,
who requested the command.
Only used in DPBOX for the TNTCOMM command.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE + (strlen(buffer) + 1)
Command   (4 Byte)
  CMD_TNTRESPONSE
Follows   (4 Byte)
  follows
Buffer    ((strlen(buffer) + 1) Byte)
  char buffer[]  


1.33 Abort Connect
------------------
(Program->PR)
A connect request started by 'usernr' shall be aborted.

Indicator (1 Byte)
  IF_COMMAND
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  LEN_SIMPLE
Command   (4 Byte)
  CMD_ABORTCON



2. Data
-------

Indicator (1 Byte)
  IF_DATA
Channel   (2 Byte)
  channel
Usernr    (2 Byte)
  usernr
Length    (2 Byte)
  1 - 256
Data      (Length Bytes)
  char data[]



3. Unproto
----------
The data will be sent to the destination last defined by CMD_SETUNPROTO.

Indicator (1 Byte)
  IF_UNPROTO
Channel   (2 Byte)
  NO_CHANNEL
Usernr    (2 Byte)
  NO_USERNR
Length    (2 Byte)
  1 - 256
Data      (Length Bytes)
  char data[]