1.  IDRIS KERMIT

Authors:    Dan  L. Eisner,  C. Steven  Mayfield,  of  the  Perkin-Elmer Corp.
            (Garden Grove, CA).  Based on the C KERMIT of Bill Catchings,  Bob
            Cattani,   Chris   Maio,   Columbia   University  with  fixes  and
            contributions from many others.  Bootstrap procedures coverted by
            Chris Lent of the Cooper Union (New York, NY)


Documentation:

            Dan  L.   Eisner,  Perkin-Elmer  Corp.(Garden  Grove, CA). Based on
            documentation by Walter Underwood, Ford Aerospace (Palo Alto, CA)
            Chris Lent, Cooper Union (New York, NY).

Version:    1.1(0)


Date:       December 5, 1986

IDRIS PERKIN-ELMER 7000 SERIES KERMIT AT A GLANCE:


Local operation:                        Yes
Remote operation:                       Yes
Transfers text files:                   Yes
Transfers binary files:                 Yes
Multiple file send:                     Yes
^X/^Y Interruption:                     No
Filename collision avoidance:           No
Timeouts:                               Yes
8th-bit Prefixing:                      Yes
Repeat character compression:           Yes
Alternate block check types:            Yes
Communications settings:                Yes
Terminal Emulation:                     No
IBM Mainframe communications:           Yes
Transaction logging:                    No
Debug logging:                          Yes
Raw Transmit:                           No
Login scripts:                          No
Act as server: (GET,SEND,FINISH)        Yes
Talk to server: (GET,SEND,FINISH)       Yes
Advanced commands for servers:          No
Command/init files:                     No
Handle file attributes:                 No
Long Packets Support:                   No
Sliding Windows Support:                No


A  sample,  working implementation of the Kermit "kernel" was written in the C
language, and widely distributed in the Kermit Protocol Manual.   This  kernel
was  intended  merely  to illustrate the protocol, and did not include a "user
interface", nor some of the fancy features like server support, 8-bit quoting,
file warning, timeouts, etc.  Several sites have added the necessary trappings
to make this a production version of Kermit, usually under the UNIX  operating
system.

The keyword style of user/program interaction favored by Kermit (program types
prompt, user types command followed by operands, program types another prompt,
etc)  is contrary to the UNIX style, so UNIX implementations have a style more
familiar to UNIX users.  C versions of Kermit are running successfully on  VAX
and  PDP-11  UNIX systems, IBM 370 compatible mainframes under Amdahl UTS, and
the SUN Microsystems MC68000-based and other workstations.

This version for the IDRIS system uses the same interface.


                                     NOTE

     After   attempting   to   conditionalize   the  UNIX  versions,  the
     conditionals  were  not  used.   The  required  interface  to  IDRIS
     required too many changes to the UNIX version.  Instead a version to
     complile and run on a IDRIS system was completed.  A  few  additions
     to  the  UNIX version were added.  These additions are 8-bit quoting

     and repeat count prefixing.

1.1 The IDRIS File system

IDRIS File Specifications

IDRIS filespecs are of the form

$   dir1/dir2/dir3/ ...  /filename

where  the tokens delimited by slashes form a path name, and by convention are
each limited to 14 characters in length.  The final token in  a  path  is  the
actual  file  name.   By convention, it is of the form name.type, but there is
nothing special about the dot separating name and type;   to  UNIX  it's  just
another character, and there may be many dots in a filename.

In the tradition of IDRIS, here's the UNIX Kermit "man page".


INAME            Kermit - file transfer, virtual terminal over tty link


SYNOPSIS        kermit -r[diutplb]

                kermit -s[fdiutplb] file ...

                kermit -g[fdiutplb] file....

                kermit -x[dviutpl]

                kermit -f[dtpl]


DESCRIPTION     Kermit  provides  reliable file transfer and primitive virtual
                terminal  communication  between  machines.    It   has   been
                implemented   on   many   different   computers.    The  files
                transferred may be arbitrary ASCII data (7-bit characters) and
                may  be  of  any  length.   Binary  (8-bit)  files may also be
                transferred under most conditions.  The file transfer protocol
                uses  small  (96 character) checksummed packets, with ACK/NACK
                responses and timeouts.  Kermit currently uses  a  ten  second
                timeout and eight retries.

                The  IDRIS  Kermit  command  line is in the style of TAR.  The
                arguments are a set of flags and, if this is  a  Send  or  Get
                operation a list of one or more files.

                Kermit  has  four modes, Send, Receive, Get and Server.  These
                modes are for file transfer.  These modes are specified by the
                first  flag,  which  should  be  s,r,g,  or  x,  respectively.
                Exactly one mode must be specified.

                The  d<integer  number>  flag  (debug) makes Kermit a bit more
                verbose.  The states Kermit goes  through  are  printed  along
                with  other traces of its operation.  A second parameter of an
                integer number must be present  with  the  d  flag.   A  value
                greater than 1 will cause Kermit to give an even more detailed
                trace.

                The  i  flag  (image)  allows  slightly  more  efficient  file
                transfer between IDRIS machines.  Normally (on Kermits defined
                to  run on IDRIS systems) newline is mapped to CRLF on output,
                CR's are discarded on input, and bytes are sent  7  bits.   If
                this  is  set,  no  mapping is done on newlines, and all eight
                bits of each byte are sent or received.  This is  the  default
                for  all  other  Kermits.   The  parity is determined from the
                hardware or the input command line and the 8-bit quote flag is
                internally  set  with  respect  to  the  parity setting.  This
                determination of the parity produces image  transfers  if  the
                receiving or sending Kermit supports the 8-bit quote mode.  If
                the image mode is not supported (by  either  side)  and  image
                mode is requested by one of the sides, the transfer is aborted
                and an error message is sent.

                The  u  flag  (upercase)  turns  off the file name conversion.
                Normally (the default) file names  are  converted  from  lower
                case  to  upper case on transfers out of the IDRIS machine and
                converted from upper case to lower case when a  file  name  is
                received by the IDRIS machine.  The u flag when off causes the
                file name to be not converted (case conversion only).

                The  t  flag  (turnaround) tells Kermit while in protocol mode
                (sending or receiving) to  wait  for  a  turnaround  character
                (XON)  from the other host after receiving every packet.  This
                is necessary to run Kermit with a half duplex host such as  an
                IBM mainframe.

                The  p<char> flag (parity) allows parity to be set on outgoing
                packets and stripped on incoming ones.   This  is  useful  for
                communicating  with  IBM  hosts  or  over  networks,  such  as
                TELENET, that usurp the parity bit.  The possible  values  for
                parity are mark, space, even, odd or none (the default).

                The  l<device  string> flag (line) specifies the tty line that
                Kermit should use to communicate with the other machine.  This
                is specified as a regular filename, like "/dev/tty1".  If no l
                option is specified, /dev/lnk0 is used.

                The  b<integer  number> flag (baud) sets the baud rate for the
                terminal line.  This means that the baud rate of the  terminal
                line  will  be  set  to the given speed.  Valid rates are 110,
                150, 300, 1200, 2400, 4800, and 9600.  The  normal  number  of
                stop bits is one except for 110 baud which is set to two.

                The  v  flag  (verbose)  allows  the  output  of informational
                messages during a get operation.  The number  of  packets  are
                displayed  along with informational messages that are normally
                present with the send and receive commands. The v flag also
		causes the version number of IDRIS Kermit to be printed.

                The  file  arguments  are  only  meaningful  to  a Send or Get
                Kermit.  The Receiving Kermit will attempt to store  the  file
                with  the  same  name that was used to send it.  IDRIS Kermits
                normally convert outgoing file names to uppercase and incoming
                ones to lower case (see the u flag).  To disable this feature,
                turn on the u flag.  If a filename contains a slash (/) Kermit
                will  strip  off the leading part of the name through the last
                slash.  There may be multiple file names on the command  line.
                If "wild cards" are included in the file name the command line
                must be passed thru the shell processor  to  expand  the  file
                names.   The  Get command passes the complete file name string
                to the remote processor and it is up to the  remote  processor
                to parse the file names (including wild-cards).


1.2 Program Operation


EXAMPLE         For  this  example  we will assume two IDRIS machines.  We are
                logged  onto  "IDRISa"  (the  local  machine),  and  want   to
                communicate  with  "IDRISb"  (the remote machine).  There is a
                modem on "/dev/tty3".

                We  want to connect to "IDRISb", then transfer "file1" to that
                machine.

We type:

*                  cu -l/dev/tty3 -s1200

cu answers

                  recv

                Now  we  dial  the  remote  machine  and  connect  the  modem.
                Anything typed on the terminal will  be  sent  to  the  remote
                machine  and any output from that machine will be displayed on
                our terminal.  We hit RETURN, get a "login:" prompt and login.

                Now we need to start a Kermit on the remote machine so that we
                can send the file over.  First we start  up  the  remote,  (in
                this  case  receiving)  Kermit, then the local, (sending) one.
                Remember that we are talking to IDRISb right now.

We type:

                  kermit r

                (there is now a Receive Kermit on IDRISb)

                We type \ (the escape character) and then the letter q to kill
                the local (Connecting) cu
We type:

                  kermit -s -l/dev/tty3 file1

                Kermit answers:

                  Sending file1 as FILE1

                When  the  transmission  is  finished, Kermit will type either
                "Send complete", or "Send failed.", depending on  the  success
                of  the  transfer.   If  we now wanted to transfer a file from
                IDRISb  (remote)  to  IDRISa  (local),  we  would  use   these
                commands:

                  cu -l/dev/tty3 -s1200

                  (connected to IDRISb)

                  kermit -s file9

                  \q (talking to IDRISa again)

                kermit -r -l/dev/tty3

                After  all  the  transfers were done, we should connect again,
                log off of IDRISb, kill the Connect Kermit  and  hang  up  the
                phone.

1.3 IDRIS KERMIT FEATURES

FEATURES        Kermit  can  interact  strangely  with  the  tty  driver.   In
                particular, a tty with "hangup on last close" set (stty  hup),
                will  reset to 300 Baud between Kermit commands.  It will also
                hang up a modem at that time.  It is better to run with  "stty
                -hup", and use "stty 0" to explicitly hang up the modem.

                The  Kermit  Protocol  uses  only  printing  ASCII characters,
                Ctrl-A, and CRLF.  Ctrl-S/Ctrl-Q  flow  control  can  be  used
                "underneath" the Kermit protocol.

                Since  BREAK  is  not an ASCII character, Kermit cannot send a
                BREAK to the remote machine.  On some systems, a BREAK will be
                read as a NUL.

                This  Kermit  does  have timeouts when run under IDRIS, so the
                protocol is stable  when  communicating  with  "dumb"  Kermits
                (that don't have timeouts).


1.4 IDRIS KERMIT ERROR MESSAGES

DIAGNOSTICS
                Diagnostics  are  of three formats.  "Kermit usage" are errors
                detected due to usage errors.  "Kermit" errors are during file
                receiving  and  abort  the program.  Messages without a prefix
                are informational messages.  A listing of errors follow:

        Kermit usage:  Invalid command line.  Not enough arguments
                Kermit was called without any arguments.

        Kermit usage:  Cannot open <device>.
                The  file  named in the line argument did not exist or had the
                wrong permissions.

        Kermit usage:  Only one command allowed -g !  r !  s !  x.
                The command line contained two commands.

        Kermit usage:  Finish with server or receive?

                The finish flag was turned on along with the server or receive
                flag.  This  usage  is  incompatable  with  each  other.   The
                receive or server is told to finish from the remote Kermit and
                not from the local Kermit.

        Kermit usage:  Improper parity call out.
                The command line p flag did not contain a 'n' or 'e' or 'o' or
                'm' or 's'.

        Kermit usage:  File name required.
                The input command line did not contain a file name as required
                by the requested conmmand (get or send).

        Kermit usage:  Bad line speed.
                The baud rate inputed was not a valid baud rate.

        Kermit usage:  Get failed.
                The Get command failed.

        Kermit usage:  Send failed.
                The Send command failed.

        Kermit usage:  Receive failed.
                The Receive command failed.

        Kermit usage:  Finish failed.
                The Finished command failed.

        Get done.
                The Get command completed.

        Send done.
                The Send command completed.

        Receive done.
                The Receive command completed.

        Finish done.
                The Finish command completed.

        Requesting <inputed file name> as <converted file name>
                The  Get  command  is stating the files that it will be using.
                If file name conversion is in effect the data output will show
                the  conversion.   The  inputed  file  name  is  what the user
                requested, The converted file  name  is  what  the  system  is
                sending to the other system.

        Kermit:  Cannot open file <file name>
                The  open  file  request  from  the  Send command could not be
                completed.  The file may not exist or the user does  not  have
                access to the file.

        Sending <typed file name> as <converted file name>
                The Send command is stating the files that it will be using.

        Receiving <received file name> as <outputed file name>
                The  receive  processor  is stating the file names that it has
                received and the file names it will be storing the data into.

        Sending <inputed file name> as <outputed file name>
                The  send  processor is stating the file names that it will be
                using in the send process.

        <integer number> / <integer number>
                The  send packet routine is showing the total count of packets
                it has sent versus the total count of error packets that  have
                been sent or received.

        Kermit:  Abort with error from remote host:
        <text from remote Kermit>
                The remote Kermit detected an error and is notifying the local
                Kermit what hat error was.


REMOTE ERRORS   Invalid server command
                A  g  packet  was  received  and  the  command  has  not  been
                implemented or the command is not valid.

                Unknown packet type
                The server received a packet which it did not recognize.

                Cannot create <file name>
                The  receiving  Kermit could not create the file being sent to
                it.

                Cannot open file <file name>
                The remote server could not open the file for sending.

                Binary file transfer not supported
                The  send-init  parameters detected that binary file transfers
                were not possible.  The parity bit is on and 8-bit quoting  is
                off and image has been requested is an example of this error.


                The debug output messages are not listed.


1.5 INSTALLATION OF IDRIS KERMIT

1.5.1	Bootstrapping from the communication line

	Two methods exist for transferring the Kermit bootstrap programs
	to the Perkin-Elmer 7000 Series computer.  One method is to
        use a terminal emulation package resident on the PE-7000 to
        "download" the two files PE7BOO.BAS and PE7KER.BOO. Perkin-Elmer
	supports the 'cu' command for terminal emulation with the 7000
        Series computer.  The 'cu' program will log characters coming into
        the RS-232 port, BUT ONLY if correctly instructed by the REMOTE host.

	The sequence is as follows:

	PE7000 User:                              Comments
        $ cu -l/dev/tty2 -s9600                   <--User calls up terminal
                                                  Emulator
        recv                                      <--PE is ready termulate
	Remote host ready                         <--Remote computer prompts
        login:j.user
        password:

        Welcome to N-IX System 3.141592 Release 2.718
			.

        $ # Well, let's assume some Unix-ish remote computer environment
                        .
                        .

        [ By some means the user constructs a procedure to type
         a backslash, a greater-than, a filename (the name the file
         will be on the PE-7000), and a carriage-return line-feed. 
         The procedure then lists a file (at 1200 baud or lower)
         and finally types a backslash, a period and a carriage-return
         line-feed sequence.  (Of course, all this must be done without
         actually typing the \> sequence during the construction!)

         The backslash greater-than filename sequence tell cu to start
         logging the terminal session to the filename given and stop
         displaying anything else.  The terminal session will renew
         with the backslash period carriage-return linefeed and
         close the logfile.]

         [ Output required from remote host ]

         \>pe7ker.bas                           <---No space between > and
               [List the pe7ker.bas file.]      <--- filename
         \.

         [On UNIX this can be done with the following Bourne shell script]
         $ cat >feedcu.sh
         # feedcu.sh
         # Usage feedcu.sh filename
         echo '\''>'$1
         cat $1
         echo '\''.'
         <control-d>
         $ # and that's all folks
         [Note that when you type the backslash in 'cu' it is not echoed
          until the next character is typed. ]

         $ # So to download pe7boo.bas go
         $ # Make feedcu.sh executable
         $ chmod 0755 feedcu.sh
         $ feedcu.sh pe7boo.bas
         \> pe7boo.sh                               <---- PE-7000 indicate
                    				    <---- transfer in progress 
         $ # When done check on the file.  The filename on the PE-7000 may
         have spaces before or after it.  You may have to download
         repeatedly to get a workable copy of pe7boo.sh
         $ exit
         [ and \q ] to quit the cu emulator. MAKE SURE TO HANG UP THE PHONE!

        The same procedure is repeated for pe7ker.boo, which is an
        text-encoded version of the pe7ker.exe program.
   
        The other manner is comparatively more simple but requires more
        of the remote host.  First start a login running on one of
        the RS-232 ports of the PE-7000, as described in Vol. 2 Section 6
        of the 7000 Series User's Guide.  Then with some other host
        (usually a PC running MS-KERMIT 2.29 or above) you login to
        the 7000 Series system and type :

		$ cat >pe7boo.bas

        and then use the ASCII uploading function, TRANSMIT, to send
        the pe7boo.bas. (Most commercial terminal emulator packages have
        some sort of ASCII upload function.)  Similarly after you've verified
        that pe7boo.bas was uploaded correctly, upload pe7ker.boo.
1.5.2   DECODING .BOO files
        
        Now that the files, pe7boo.bas and pe7ker.boo are on the PE-7000,
        type the following command:

	$ basic -rpe7boo.bas

        and after about 10 minutes the file PE7KER.EXE will be produced.
        Please note the file name is in UPPERCASE.  The next task is to
        retransfer pe7ker.boo with PE7KER.EXE so that you are assure
        of a good working copy.  Lastly, so you won't have to repeat this
        may a backup and put it somewhere safe and away from the computer
        area.

        Note also that the .BOO format is also used to bootstrap the MS-DOS
        version of Kermit and is compatible with the programs MSBPCT.BAS and
        MSBMKB.EXE.

1.5.3   PHONE

	PE7PHO.EXE is a Hayes modem control program for the PE-7000.
        PE7PHO.BOO is a .BOO encoded version of PE7PHO.EXE.

        To convert PE7PHO.BOO to PE7PHO.EXE do the following steps:

            [Bootstrap procedure for PE7PHO.EXE]

             $ basic

             Perkin-Elmer 7000 Series Computer Basic  ver.  1.30
             (c) 1983 PERKIN-ELMER  All Rights Reserved
             (c) 1981, 1982 Hemenway Corp.  All Rights Reserved

             ready
             load "pe7boo.bas"

             ready
             list 65
             65 k$="pe7ker.boo":rem filename case significant

             ready
             65 k$="pe7pho.boo"
             run
             PE7BOO.BAS Version 2.3a (Derived from IBM-PC MSBPCT.BAS)
             PE7PHO.EXE
             Outputting to PE7PHO.EXE
             Null:         14 
             Null:           2 
             Null:       3 
             Null:        2 

                            [ And so on for five minutes ... ]

             Null:       4 
             Null:       4 
             Null:       5 

             Processing complete, elapsed time: 02:11:58 to 02:16:41
             Output in PE7PHO.EXE
 
             ready

             system

             basic terminated
             $ chmod +x PE7PHO.EXE
             $ ./PE7PHO.EXE
             Phone usage: No arguments given.
             $

             [End of PE7PHO.EXE bootstrap procedure ]

1.5.4 USING THE PHONE PROGRAM

	Phone is designed to intialize dial and hangup a Hayes modem attached
to a serial port. The command line options are listed following:

   Usage:
	$ PE7PHO.EXE -i -d -v -l -b -a -p -h -c
 
   where   i=init modem <flag>, d=debug level <number>, v=verbose <flag>,
 		l=line <device>, b=baud rate <number>, a=answer <flag>,
 		p=phone number <string>, h=hang-up request <'a' or 'o'>,
 		c=direct connect <'a' or 'o'>
 
1.5.4.1 Sample session

The following session show dialing with PHONE in verbose mode, connecting
for a terminal session with 'cu' and then hanging up the phone with PHONE.

          $ PE7PHO.EXE -v -l/dev/tty0 -b1200 -p 5551212
          Phone: Initializing the modem
          Phone: Dialing 5551212
          Phone: Connect at 1200 Baud
          $ cu -l/dev/tty0 -s 1200
          recv

          [ And the terminal session starts]

                 ...

          [ Continues]
      
                 ...

          [ and ends]
          \q                                     <--- to quit cu type '\q'
          $ # Now to hangup the phone
          $ PE7PHO.EXE -v -l/dev/tty0 -b1200 -ho
          Phone: Hanging up
          $ # Done.

          [End of example]
1.6  RECOMPILING FROM SOURCE

        If it possible to transfer the text files which make up
IDRIS Kermit and PHONE, PE7INC.H, PE7TTY.H, PE7STD.H, PE7SYS.H,
PE7MAI.C, PE7PTA.C, PE7PTB.C, and PE7PHO.C, the source may be
re-compiled using the shell script routines (and the optional 'C'
compiler). The scripts PE7KER.MAK and PE7PHO.MAK will reproduce
a PHONE and KERMIT executable.


1.7  FUTURE CONSIDERATIONS

	With the generality of the current UNIX C-Kermit it may be
possible to merge the IDRIS Kermit into the C-Kermit distribution along
the lines of the Macintosh and VAX/VMS C-Kermit's.  If 'C' becomes
popular on the PE-7000, more development may be seen.